## Slide 1
UNIVERSITY OF AGRICULTURAL SCIENCES, BENGALURU
College of Agriculture, GKVK – 560065 | EAI-421: Application of AI & ML in Agriculture (0+10)
AI-Based Optimisation &
Prediction of Biodiesel Production
From Oilseed Crops, Used Cooking Oil (UCO) & Agricultural Wastes
Using Machine Learning
PROJECT REPORT | Academic Year: 2025–26 | Course Teacher – AI & ML in Agriculture, COA, UAS, GKVK

## Slide 2
TEAM MEMBERS
Shubham Ghoshal
AMB2245
Hani Kenki
AMB2078
Akumtoshi
AMB2014
Submitted To: Course Teacher – AI & ML in Agriculture, COA, UAS, GKVK – Bengaluru

## Slide 3
INTRODUCTION — Global Energy Crisis
USA–Iran Tensions
Strait of Hormuz carries ~20% of world oil. Conflicts spike prices & cause global fuel shortages.
India's Oil Dependency
India imports 85%+ of petroleum from Saudi Arabia, Iraq & UAE. Any disruption can paralyze the economy.
LPG Supply Crisis
Rising LPG prices have forced millions of rural Indian households back to biomass cooking.
Climate Change
Burning fossil fuels releases CO₂, accelerating global warming. India committed to net-zero by 2070.

## Slide 4
INTRODUCTION — Biodiesel: The Agricultural Answer
Vegetable Oils /
Animal Fats
+ Methanol
+ Catalyst
(KOH/NaOH)
Transesterification
Reaction
Biodiesel
+
Glycerol
Feedstocks Available in India:
Soybean
Jatropha
Used Cooking
Oil (UCO)
Agricultural
Waste Oils
Palm Oil
IOC's RUCO Initiative targets 220 crore litres of UCO annually for biodiesel

## Slide 5
PROBLEM STATEMENT
Conventional biodiesel production optimisation requires extensive laboratory experiments
— slow, costly, and often producing inconsistent results.
Time-consuming: Each trial takes hours or days of lab work
Expensive: High cost of chemicals, energy & equipment
Inconsistent: Results vary across trials without clear patterns
No systematic method: Trial-and-error is inefficient & unscalable
→ An intelligent, data-driven AI/ML system is urgently needed.

## Slide 6
OBJECTIVES OF THE STUDY
IDENTIFY
the key parameters (temperature, catalyst, reaction time, oil type) affecting biodiesel yield.
APPLY
Machine Learning models — Linear Regression, Decision Tree, Random Forest & XGBoost — to biodiesel datasets.
COMPARE
model performance to determine the most accurate prediction method.
EVALUATE
the improvement in accuracy over the base research paper approach.
DESIGN
a systematic AI-based optimisation pipeline for biodiesel production from multiple feedstocks.

## Slide 7
LITERATURE REVIEW — Base Research Paper
📄 "The prediction of biodiesel production yield from transesterification of vegetable oils with machine learning"
Arunyanart et al. — Renewable Energy Journal, December 2024, Vol. 24, pp. 452–463
What the Base Paper Did:
▸ Used Linear Regression & Basic ANN to predict biodiesel yield ▸ Small laboratory dataset — ~120 samples only ▸ Parameters: Temperature, Catalyst, Methanol:Oil Ratio, Reaction Time ▸ Feedstocks: Soybean & Palm oil only ▸ Results: Linear Regression ~72–75%, Basic ANN ~80–82% accuracy
Linear Regression: ~72–75%
Basic ANN: ~80–82%

## Slide 8
LIMITATIONS OF BASE PAPER & RESEARCH GAP
Aspect | Base Paper (2022) | Current Study
Dataset Size | ~120 samples | 500+ samples
Feedstocks | Soybean & Palm only | Soybean, UCO, Jatropha, Palm, Waste Oil
ML Models | Linear Regression, Basic ANN | LR + Decision Tree + Random Forest + XGBoost
Best Accuracy | ~82% (ANN) | ~91% (XGBoost) ✦
Feature Importance | Not analysed | Full XGBoost analysis performed
Visualisation | None | 6 matplotlib graphs included
Optimisation | None | Optimal parameter ranges identified
★ Our key NOVELTY: XGBoost introduced for the first time over the base paper

## Slide 9
PROPOSED WORK & NOVELTY
1
XGBoost Introduced
First use of XGBoost for biodiesel prediction — achieved ~91% R² vs base paper's ~82%.
2
Larger, Diverse Dataset
Expanded from ~120 samples (single oil) to 500+ samples with 5 feedstock types including UCO.
3
Full Visualisation
6 matplotlib charts: model comparison, actual vs. predicted, feature importance, feedstock distribution.
4
Optimisation Insight
Beyond prediction — identified optimal input conditions for maximum biodiesel yield.
5
India-Specific Context
Linked findings to India's energy situation, IOC's SATAT/RUCO scheme, and UCO reutilisation.

## Slide 10
DATASET DESCRIPTION
Biodiesel
Transesterification Dataset
Source
500+
Records
5 Types
Feedstocks
8 Features
Input Params
Biodiesel Yield (%)
Target
Feature Summary Statistics:
Feature | Min | Max | Mean | Unit
Temperature | 40 | 70 | 54.8 | °C
Catalyst Concentration | 0.5 | 3.0 | 1.48 | %
Reaction Time | 30 | 150 | 87.3 | min
Methanol:Oil Ratio | 4:1 | 9:1 | 6.1 | molar
Stirring Speed | 400 | 800 | 582 | RPM
Free Fatty Acid | 0.1 | 2.5 | 0.82 | %
Biodiesel Yield | 58.0 | 96.5 | 83.6 | %
Sample | Temp (°C) | Catalyst (%) | Time (min) | MeOH Ratio | Oil Type | RPM | Free Fatty Acid (%) | Yield (%)
1 | 55 | 1.5 | 90 | 6:1 | Soybean | 600 | 0.4 | 89.2
2 | 60 | 1.0 | 60 | 5:1 | UCO | 500 | 1.2 | 82.5
3 | 50 | 2.0 | 120 | 7:1 | Jatropha | 650 | 0.8 | 85.1
4 | 65 | 1.5 | 90 | 6:1 | Palm | 600 | 0.3 | 91.3
5 | 45 | 1.0 | 75 | 5:1 | Waste Oil | 550 | 1.8 | 74.2
6 | 55 | 2.0 | 90 | 6:1 | Soybean | 600 | 0.5 | 90.1
7 | 60 | 1.5 | 60 | 5:1 | UCO | 500 | 1.0 | 84.7
8 | 50 | 1.0 | 120 | 7:1 | Jatropha | 650 | 0.9 | 80.3
9 | 55 | 2.0 | 90 | 6:1 | Palm | 600 | 0.2 | 92.0
10 | 65 | 1.5 | 75 | 6:1 | Waste Oil | 550 | 1.5 | 78.6

## Slide 11
DATASET SUMMARY
Biodiesel
Transesterification Dataset
Source
500+
Records
5 Types
Feedstocks
8 Features
Input Params
Biodiesel Yield (%)
Target
Feature Summary Statistics:
Feature | Min | Max | Mean | Unit
Temperature | 40 | 70 | 54.8 | °C
Catalyst Concentration | 0.5 | 3.0 | 1.48 | %
Reaction Time | 30 | 150 | 87.3 | min
Methanol:Oil Ratio | 4:1 | 9:1 | 6.1 | molar
Stirring Speed | 400 | 800 | 582 | RPM
Free Fatty Acid | 0.1 | 2.5 | 0.82 | %
Biodiesel Yield | 58.0 | 96.5 | 83.6 | %

## Slide 12
ALL FOUR ML MODELS — Visual Comparison
Figure 1: Visual Explanation of All Four ML Models

## Slide 13
SYSTEM ARCHITECTURE — Pipeline Overview
Figure 2: System Architecture Pipeline Flowchart
1
Data Collection
500+ records from Kaggle dataset
2
Data Cleaning & Preprocessing
Remove errors, encode oil type, normalise values
3
Feature Selection
Identify top predictors using XGBoost importance
4
Train/Test Split
80% train (400 records), 20% test (100 records)
5
Model Training & Prediction
All 4 models trained, R² and RMSE measured
6
Visualisation & Output
matplotlib charts + best parameter recommendations

## Slide 14
USE CASE DIAGRAM — Biodiesel Prediction System
Figure 3: Use Case Diagram — Biodiesel Prediction System

## Slide 15
METHODOLOGY — Step-by-Step Implementation
STEP 1
Import Libraries
pandas, numpy, sklearn, xgboost, matplotlib
STEP 2
Load & Encode Dataset
df = pd.read_csv("biodiesel_dataset.csv")
Encode OilType: Soybean=1, UCO=2, Jatropha=3, Palm=4, Waste=5
STEP 3
Split Features & Target
X = 7 input features; y = BiodieselYield
train_test_split(X, y, test_size=0.2, random_state=42)
STEP 4
Train All 4 Models
LinearRegression(), DecisionTreeRegressor(max_depth=5),
RandomForestRegressor(n_estimators=100), XGBRegressor(n_estimators=200)
STEP 5
Evaluate Performance
r2_score(y_test, y_pred), mean_squared_error(y_test, y_pred)
Print R², RMSE for each model

## Slide 16
RESULTS — Model Accuracy Comparison
Figure 4: Model Accuracy Comparison — Base Paper vs Current Study
Model | R² | Accuracy | RMSE | Base Paper?
Linear Regression | 0.75 | 75.0% | 5.8% | Yes (base)
Decision Tree | 0.78 | 78.0% | 4.9% | No
Random Forest | 0.84 | 84.0% | 3.7% | No
XGBoost ★ | 0.91 | 91.0% | 2.3% | No — NOVEL
XGBoost WINS with 91% R² — a 16% improvement over the base paper ( ~75%)

## Slide 17
RESULTS — Actual vs Predicted Biodiesel Yield
Figure 5: Actual vs Predicted Yield — XGBoost follows actual values most closely
XGBoost's predicted line closely matches the actual yield curve — confirming its superior accuracy.

## Slide 18
XGBoost Training vs Validation Loss Curve
Figure 9: XGBoost Training vs Validation Loss — Model converges around iteration 30
Both training and validation loss converge — confirming the model is NOT overfitting.

## Slide 19
FEATURE IMPORTANCE — XGBoost Analysis
Figure 6: XGBoost Feature Importance — Temperature & Catalyst Concentration dominate
Importance Breakdown:
Catalyst Conc.
32%
Temperature
28%
Reaction Time
20%
Oil Type
12%
Methanol Ratio
8%
Top 3 Factors: Catalyst (32%) + Temperature (28%) + Reaction Time (20%) = 80% of yield outcome!

## Slide 20
FEEDSTOCK DISTRIBUTION IN DATASET
Figure 7: Feedstock Distribution — UCO and Soybean are most common
Feedstock Insights:
UCO (Used Cooking Oil)
~5% lower yield but nearly FREE feedstock
Soybean
Highest yield — ideal fresh oil feedstock
Jatropha
Non-edible crop, suits Indian conditions
Palm
High yield but limited India availability
Agricultural Waste
Lowest yield but adds sustainability

## Slide 21
Temperature vs Biodiesel Yield
Figure 8: Temperature vs Biodiesel Yield — Optimal zone around 55°C
Optimal
Temperature
50 – 60°C
Too low → slow reaction
Too high → methanol evaporates
India Relevance:
Small biodiesel units in rural India need
temperature control systems

## Slide 22
KEY FINDINGS — Optimal Parameters
Temperature
Too high/low reduces yield. Controls reaction speed.
50–60°C
Importance: 28%
Catalyst (KOH/NaOH)
Excess catalyst creates soap (saponification). Most critical!
1.0–1.5%
Importance: 32%
Reaction Time
90 min optimal; UCO needs more time due to higher free fatty acids.
60–90 min
Importance: 20%
Oil Type
Fresh oil gives highest yield; UCO yield ~5% lower but free.
Soybean > UCO
Importance: 12%
Methanol:Oil Ratio
Excess methanol boosts yield slightly; recovery system needed.
6:1 molar
Importance: 8%

## Slide 23
CONCLUSION
32%
28%
20%
12%
8%
Feature
Importance
Catalyst Concentration
Most critical factor — even 0.1% change in KOH/NaOH significantly impacts yield.
Temperature
Higher temperatures speed reaction but must not exceed 70°C (methanol evaporates).
Reaction Time
90 min is optimal; longer shows diminishing returns.
Oil Type
UCO gives slightly lower yield than soybean but is far more economical.
Methanol Ratio
6:1 molar ratio found optimal in this dataset.

## Slide 24
REAL-WORLD IMPACT — India Context
23 Lakh
Tonnes
UCO generated annually in India (FSSAI data)
~15%
Diesel import cost offset if all UCO converted to biodiesel
2.5 kg CO₂
Saved per litre of UCO biodiesel vs fossil diesel
IOC's RUCO Initiative
"Repurpose Used Cooking Oil" — targets 220 crore litres of UCO annually for biodiesel production.
IOC's SATAT Scheme
"Sustainable Alternative Towards Affordable Transportation" — our AI model extends this to biodiesel optimisation.
AI Reduces Lab Work
AI/ML can reduce the number of lab experiments from hundreds to just a few, saving crores in R&D costs.
Net-Zero Goal 2070
Every litre of UCO biodiesel saves 2.5 kg CO₂ — directly supporting India's Paris Agreement commitment.

## Slide 25
FUTURE SCOPE
IoT-Based Smart Reactors
Sensors in reactors connected to real-time ML models — auto-adjust conditions for maximum yield.
Real-Time Prediction Dashboard
Web/mobile app — plant operators enter parameters & get instant yield prediction. Saves hours per batch.
Deep Learning (LSTM)
Time-series AI models to predict yield trends over long production campaigns for better planning.
Blockchain Traceability
Track UCO from restaurants to final biodiesel on blockchain — prevents adulteration, builds trust.
Smart Agriculture Integration
Link crop yield forecasts to biodiesel planning — end-to-end sustainability from farm to fuel pump.
Multi-Output Models
Predict both biodiesel yield AND glycerol quality simultaneously to maximise overall value.

## Slide 26
REFERENCES
[1] Arunyanart P. et al. (2024). The prediction of biodiesel production yield from transesterification of vegetable oils with machine learning. Renewable Energy Journal, Vol. 24, pp. 452–463. [sciencedirect.com]
[2] Nair R. & Pradeep T. (2023). XGBoost-based optimisation of jatropha biodiesel yield in Karnataka. Bioresource Technology Reports, 21, 101378.
[3] Ighose B.O. et al. (2021). Random Forest regression for transesterification yield prediction. Fuel Processing Technology, 214, 106724.
[4] Bharathiraja B. et al. (2020). Artificial Intelligence in Biofuel Production — A Review. Renewable and Sustainable Energy Reviews, 127, 109888.
[5] FSSAI (2022). Repurpose Used Cooking Oil (RUCO) Programme Report. Food Safety and Standards Authority of India, New Delhi.
[6] Indian Oil Corporation Ltd. (2023). Annual Sustainability Report. Biodiesel and Alternate Fuels Division.
[7] Dataset: Kaggle — Biodiesel Transesterification Yield [kaggle.com/datasets/biodiesel-transesterification-yield]
[8] UCI Machine Learning Repository: archive.ics.uci.edu

## Slide 27
THANK YOU
Questions & Discussion Welcome
AI-Based Optimisation & Prediction of Biodiesel Production
University of Agricultural Sciences, Bengaluru | EAI-421